## Slide 1: Nyon-data, a Fall Detection Dataset from a Hinged Board Apparatus
The 8th Smart City Applications International
Conference
Rogério Dionísio, Ana Rafaela Rosa and Cassandra Sofia dos Santos Jesus
Polytechnic Institute of Castelo Branco, Portugal
October 4th, 2023 – ESTP Cachan, Paris, France

## Slide 2: The team

## Slide 3: Summary
Objectives
Dataset creation
Application with a fall detection algorithm
Results and analysis
Final comments

## Slide 4: Rationale and objectives
Monitor elder fall detection and create a warning system
Wearable device
Limited contact due to COVID-19
Objectives:
  Generate a dataset focused on the Portuguese population
  Use an apparatus that mimics a human fall
  Test the dataset with a fall detection algorithm
Notes: In 2021, Portugal ranked fourth on the list of the oldest population countries in Europe.

## Slide 5: Datalogger Circuit
An Arduino UNO board;
A 3-Axis digital accelerometer (ADXL345);
A micro-SD card reader breakout board (Adafruit);
A push-button to control the start and completion of the data collection process;
A green LED to signal when the SD-card is recording;
A red LED to signal that the program was stopped successfully;
Several resistors for current limitation of the LED and the push-button;

## Slide 6: Hinged platform
Emulate a fall event.
Measurement levels:
Ankle (7 cm)
Knee (48 cm)
Hip (89 cm)
Measurement angles:
30º
45º
90º

## Slide 7: Dataset description
Nyon_data Folder
Ankle_30.csv
time (s)
Ankle_45.csv
Acc. X (g)
Acc. Y (g)
Acc. Z (g)
Ankle_90.csv
Hip_90.csv
...
Knee_30.csv
https://github.com/rdionisio1403/Nyon/
3 fall events
for each file

## Slide 8: Fall Detection Algorithm
Differential Sum Vector Magnitude
  Threshold algorithm
  3 axis accelerometer (x, y and z)
Kim, N. H., & Yu, Y. S. (2013). Fall recognition algorithm using gravity-weighted 3-axis accelerometer data.
Journal of the Institute of Electronics and Information Engineers, 50(6), 254-259

## Slide 9: Receiver Operating Characteristic (ROC)
Binary classification
Best Threshold

## Slide 10: Results
Dataset file | AUC | Adsvm best threshold | FPR | TPR
hankle_30.csv | 83.1 % | 0.35 | 13.6 % | 92.5 %
hankle_45.csv | 79.0 % | 0.30 | 14.4 % | 90.0 %
hankle_90.csv | 76.0 % | 0.20 | 18.6 % | 90.5 %
knee_30.csv | 72.4 % | 0.35 | 11.7 % | 87.7 %
knee_45.csv | 62.8 % | 0.25 | 14.0 % | 78.5 %
knee_90.csv | 72.0 % | 0.40 | 10.0 % | 99.8 %
hip_30.csv | 87.0 % | 0.30 | 15.0 % | 93.7 %
hip_45.csv | 82.3 % | 0.40 | 15.2 % | 81.0 %
hip_90.csv | 80.3 % | 0.25 | 20.3 % | 88.2 %
Mean value | 77.2 % | 0.31 | 14.8 % | 89.1 %
Std Deviation | 7.3 % | 0.07 | 3.16 % | 6.43 %
Area Under the Curve: 77.2 %
Best Threshold (DSVM): 0.23
  FPR = 14.8 %
  TPR = 89.1 %
No clear correlation between the results and the sensor position or angle.

## Slide 11: Final comments
The Arduino UNO platform is simple to program but powerfull enough to fullfill the objectives of the datalogger.
  Limitation: Sampling time
A new device is under development, battety powered and lightweight (Arduino Nano Sense)
  Energy restrictions
  Low computational complexity
  Simple algorithm
  WiFi / Bluetooth

## Slide 12: Thank you for your Attention!
rdionisio@ipcb.pt
The 8th Smart City Applications International
conference